BOP NOTES

BOP is B29 configured for the Amstrad CPM3
Seven Bugs have been removed.

1: The MOVE tagged to different user command did not work.  As delivered it gave 
a BDOS error if you were lucky and erased all the files if you were unlucky.  I 
nulled 3A AD 3A 32 5C 00 at byte 1618.
      There is another more subtle and more dangerous bug. The algorithm used 
may leave an erased FCB in the directory at a lower address than the new FCB. In 
that case BDOS may overwrite parts of the moved file. I have changed the routine 
(from 1615H to 1686H) so that it only works on single extent files, for larger 
files it branches to an error message at 115H and aborts. The problem is that 
the original FCB's must be set to erased status BEFORE the new ones are copied 
to disk. Then the new FCB's either appear at a lower directory address or 
overwrite the old ones. To achieve this the routine should copy all the extents 
to a variable length buffer then erase original and then recopy the whole 
buffer. B29 only uses a single buffer FCB area 32 bytes long. So I have not been 
able to do this.

2: The show disc space command gave incorrect values. I nulled 3A D4 3A at byte 
2436 to remove an unnecessary multiplication (luckily the routine does not 
multiply by 0!).

3: B29 hangs the system if entered with a user number as a command tail (though 
it accepts *). I have made it ignore the user number by changing Byte 260: 41 DA 
instead of 2A CA. This causes it to check whether first character is above 'A' 
and log the default disk if not.

4: It also hangs if entered from an empty user number or trying to access an 
empty drive. Cured with patch at 010E. At Byte 1B67: C3 0E 01/C3 2A 1A. At 10E: 
21 28 03 E3 C3 2A 1A (this sets return address on the stack to 328).

5: The File size is occasionally incorrectly calculated (when the number of 
sectors is exact multiple of 8. Corrected in line, at 327A 00/3C (delete an INC 
A) and at 3286 CA 8A 32 13 3A D4 3A FE 01 instead of CA AA 32 3A D4 3A FE 01 13. 
The new code jumps around an increment DE if exact multiple rather than jumping 
elsewhere.

6: The file copy removed all attributes (SYS, R/O etc) like NSWP205.  To prevent 
this, I replaced conditional jump to the verify routine at Byte 35A1 by a jump 
to Byte 103: C3 03 01 instead of CA D8 35) There I replaced the message  'Nosey 
aren't YOU' by a patch first performing a conditional call to verify and then 
setting the file attributes. The patch is: CC D8 35 01 52 3B 0E 1E C3 05 00).  
For a reason that escapes me, B29 sometimes still stripped the attributes 
even on mass copy. That was cured at the cost of producing some strange letters 
in the copy command by changing the mask at Byte 1099 from 7F to FF.

7: Sometimes BOP hangs on X command. Replaced routine by warm boot: at 0381 CA 
00 00/ CA AC 37.

Two sources of irritation have been removed.

1: The gratuitous insults have been deleted from messages.
2: The multiple beeps at every occasion have been removed.

I have also set BOP so that the help message (? or /) only appears when requested 
and not every time you log a new disk (Bytes: 031D and 1AD4:43 06 instead of F7 
05 and nulled CD F7 05 at Byte 2439).

The printer codes have been set to choose 12pitch, which also sets left margin 
at 12, continous stationary and 17pitch. Reset from PTR control mode.  Single 
sheet cannot be set directly, because it requires ESC $, and $ is interpreted as 
"end of string".

Hints.

Codes can be sent to the printer without any file by choosing the p option with 
no files tagged (p prints tagged files).
Use + to print a single file This command which prompts for number of copies up 
to 99 is not evident from menu).
In copying (mass or single) pressing <ENTER> or <RETURN> twice has the effect of 
answering 'No' to the verify query.

Comparison with NSWP

In the extra 3K B29 offers:
Hex dumping (H and automatic for .COM files). Nswp could produce strange results 
if you tried to View such files.
Library sweep. Position cursor on .LBR file and type V. This is excellent, but 
you cannot build libraries, you still need NULU for that.
Improved printing: print tagged files, set up printer, file name as header, page 
numbering, (page length 56 lines), multiple copies of single file, printing as 
hex for non-text files.
Change user for tagged files. This replaces the clumsy method with mass rename 
used by NSWP.

It lacks:
Squeeze facility: B29 can only unsqueeze..
Erase untagged files: mass erase only for tagged files and no query.
Rename file to different user group: use the new N command.
Set Archive (used by pip and for date stamping) and User defined (used by 
PROTEXT) attributes.
Stay in * mode.
Show size of tagged files in 1K units.

Oliver Pretzel December 88.